Key Distribution Protocols Based on Extractors Under the Condition of Noisy Channels in the Presence of an Active Adversary

Victor Yakovlev, Valery Korzhik, Guillermo Morales-Luna, Mihail Bakaev

Abstract. We consider in this paper the information-theoretic secure key distribution problem over main and wire-tap noise channels with a public discussion in presence of an active adversary. In contrast to the solution proposed by ourselves for a similar problem using hashing for privacy amplification, in the current paper we use a technique of extractors.

We propose  modified key distribution protocols for which we prove explicit estimates of key rates without the use of estimates with uncertain coefficients in notations .

This leads in the new conclusion that the use of extractors is superior to the use of hash functions only with the very large key lengths (l)(of order l>105 bits) .

We suggest hybrid key distribution protocols consisting from two consecutively executed stages. At the fist stage it is generated a short authentication key based on hash function, whereas at the` second stage it is generated the final key with the use of extractors. We show that in fact the use of extraction procedure is effective only at the second stage. We get also constructive estimates of the key rates for such protocols.

Index Terms: Authentication, cryptography, extractors, information-theoretic security, key distribution, privacy amplification, wire-tap channel.

- Introduction

Advances in design and implementation of quantum computers [1] as well as design of super-fast multiprocessor conventional computers threat some conceptually secure cryptosystems. Hence perfect one-time pad ciphers proposed by Shannon [2] are necessary. But the use of perfect ciphers requires key lengths proportional to messages [3]. This inconvenience can be solved with the use of key distribution over communication channels protected from eavesdropping. There are several approaches in order to remove (or at least to control) an eavesdropping on the keys:

-	quantum channels [4],

- methods based on fluctuation of radio wave channels [5,6,7,8],

- Wyner’s concept of wire-tap channel,

- key generation by hashing of random string initially distributed over noisy channels [13-26].

In the current paper, we follow the last approach. The most advanced results in this setting, under the condition of an active adversary have been obtained by Maurer and Wolf. They proposed several key distribution protocols [15-23] and made a performance comparison of asymptotic and non-asymptotic key rates for a given level of key security.

We considered in [26] some modification of Maurer and Wolf MW-protocol consisting using a non-interactive authentication algorithm, called by ourselves the -protocol, instead of the request-response algorithm presented in [21]. In the same paper [26], we proposed also the -protocol that differs from the -protocol in absence of the hash function transmission over public discreet channel because the hash function can be formed from the string which users have got just after the execution of the initialization phase. Using the -protocol entails an increasing of the key rate in several cases. We proposed also in [26] the so called and -protocols in which special initially distributed short keys are used in order to provide authentication procedures over public discussion channels (PDC).

Hybrid protocols comprising pairs of sequentially executed protocols (α, ), (β, ), (α, ), (β, ) were investigated in [26]. The first protocol in each pair is used to generate authentication key, whereas the second one provides a generation of the main secret key for encryption/decryption given the authentication key. The relation among the key rates and a comparison of protocol performance evaluation were also introduced.

The main feature of the protocols considered in [26] is their strict constructiveness because the parameters determining their efficiency do not contain unknown coefficients typical for Ο, Ω ,Θ-estimations.

Our contribution and novel content in the current paper are the following:

1. We propose new (modified) key distribution protocols using extractors. We prove explicit estimates of key rates without the use of estimates of uncertain coefficients in Ο,Ω,Θ-estimations. (In [26] we solved the similar problem using hash functions instead of extractors).

In contrast to [21], we consider a scenario where legal users are able to receive raw bit strings over noisy channels and as a consequence they are pair wise distinct. This entails the need to send check symbols from user A to user B in order to agree the raw bit strings received by legal users. By the same reason, we have changed the authentication algorithm: instead of a request-response algorithm [21], we use a non-interactive one based on the authentication code.

A consideration of non-asymptotic case leads us in the new conclusion that the use of extractors is superior to the use of hash functions only with for very large key lengths (l) of the order of 105 bits.

2. We suggest hybrid key distribution protocols consisting of two consecutively executed stages. At the first stage, a short authentication key based on a hash function is generated, whereas at the second stage, the final key using extractors is generated. We show that in fact the use of an extraction procedure is effective only at the second stage. We get also explicit estimates of key rates for such protocols.

3. We prove also an asymptotic behavior of the key rates for all considered protocols that allows to compare the potential efficiency of them with the potential efficiency of protocols considered here and in [26].

The outline of this paper is the following: Section II contains the preliminaries and descriptions of the main procedures to be used in key distribution protocols. In Section II-A we describe the model of key distribution based on noisy wire-tap channels in the presence of an active adversary and we introduce the main criteria for key distribution protocol efficiency. We introduce main procedures as error correction, authentication and privacy amplification (based both on hashing and extraction).

In section III we describe the αext -protocol, and the new key distribution βext-protocol without transmission of the extractor’s seed on the public discussion channel and we prove their main features.

In section IV we present a modification of the previous α΄ext- and β΄ext-protocols under the condition that initially the legal users share short authentication keys.

In section V we describe the so called hybrid protocols as combinations of different pairs of single protocols and estimates their performance evaluation.

In section VI we conclude the paper.

II.  Main notions and procedures involved in the key distribution protocol

- Model for key distribution and the main criteria for protocol efficiency

Let us consider the model of key distribution between a legal user, Alice (A), and another user, Bob (B), in the presence of an active adversary, Eve (E), assuming that initially the legal users do not have shared secret keys. The key distribution protocol (KDP) consists of two phases: initialization and key generation.

In the KDP initialization phase, A, B, and E receive random i.i.d. sequences  ,,, respectively, such that for each i,   and (fig 1.) . One of the methods to provide legal users A, B with the sequences X, Y is to generate the truly random sequence  by some trusted party, say source S, and then to transmit it to the legal users A and B over noisy channels (source model [13], [16]). We will assume that A and B receive the sequences X, Y over binary symmetric channels (BSC) without memory with error probabilities , , while the adversary E receives the sequence Z over a BSC with error probability . It is easy to see that if the original sequence S is truly random then the same property holds for the sequences X, Y and Z. (Examples of practical implementation of the initialization phase in real world can be found in [26]). In this phase it is natural to assume that the adversary is unable to intervene the transmission from S to A and B.

Fig.1. Model of key distribution protocol over noisy legal channels in presence of an active adversary

The key generation phase consists in an information exchange over a public discussion channel (PDC) with a goal to share eventually the final key. We note that the use of PDC is necessary in order to send check symbols to test the agreement of the strings X and Y and sometimes for the parameters of the hash function or extractor seed transmission (see details in  the following sections). The adversary E can receive all information transmitted over the PDC. We assume also that the PDC’s between legal users and E are binary noiseless channels (if E does not intervene in transmission). However E can change or replace this information as desired and therefore it is necessary to authenticate messages transmitted over a PDC in order to detect any intervention of E and to reject suspicious messages.

Let us define the following parameters of the key distribution protocol characterization:

l:  the key length (the number of bits which are contained in the keys К a and Kb).

I(Ka, U):   the amount of Shannon’s information in possession of the adversary E about the final key KA after receiving all acceptable information U, including the sequence Z and the other messages transmitted over the PDC.

Pe = Pr(Ка ≠ Kb):    the probability of legal users key disagreement.

Pf :   the probability of false rejection of the KDP protocol (when A or B falsely believe that E has intervened the PDC).

Pd: the probability of deception false information provided by E during information transmission over PDC (it can result in an opportunity to fix a key between any legal user and E although leaving the legal user on the belief that he (she) has shared a key with his (her) legal partner).

Rk:    the key distribution rate (the ratio of the key length l to the length of sequences X, Y),

.                                                              (1)

It is reasonable to impose the following conditions on KDP:

| l= , | (2) |
| --- | --- |
| , | (3) |
| , | (4) |
| , | (5) |
| , | (6) |

where lreq denotes the required key length and the superscript adm stands for admissible parameter value. We will say that the above conditions are requirements of the KDP. The efficiency of the KDP will be estimated by the key rate Rk and then among all protocols satisfying (2)-(6), we will select the most efficient making Rk to attain its largest value. As we will show later, some inequalities (3)-(6), may randomly hold. Then an additional requirement can be stated as

Prisk <  ,                                                        (7)

where is the probability that at least one of the inequalities (3)-(6) does not hold.

B. Known asymptotic results regarding key rates

Let us denote by R*, R** the maximum achievable key rates in a KDP between the legal users under the condition of a passive or active adversary, respectively. In papers [16], [18], [21], [23] the proofs of these values were presented. For the source model of the wire-tap channel with initialization phase in the KDP using BSC with probabilities πA, πB, πE  the following theorem holds:

Theorem 1 (see [23]): If πE > πA  and πE > πB  , then R* = R**. If either πE ≤  πA  or πE ≤ πB  then R** = 0.

We note that under the conditions πE > πA  and πE > πB, the users A and B either share the key or they may detect interception in the case of E’s intervention. This fact cannot be interpreted as a defect of KDP because E can use even a simple strategy: she tries to break off the PDC between legal users in order to impede the completion of the KDP. Let pm, denote the probabilities of disagreements among the sequence pairs (X,Y), (X,Z), (Y,Z) respectively. Then

|  | (8) |
| --- | --- |

It is easy to see that if πE > πA   then  and similarly if πE > πB   then . We will consider the worst case for legal users as .

After the execution of the initialization phase the source model is reduced to channel model where user A sends the sequence  to user B who receives it as , whereas E receives  as . Then the probability of error on the main virtual BSC between A and B is  and the probability of the wire-tap virtual channel from A to E is . (PDC keeps the same after such reducing source model to channel model.)

Theorem 2 [23]: In the channel model setup with probabilities ,  the maximum key distribution rate is

| , | (9) |
| --- | --- |

where

|  | (10) |
| --- | --- |

is the entropy function.

C. Error correcting codes

Let C  be a binary linear error correcting -code and let  be a string consisting of r check symbols. It has been proved in [30] that if the information symbols are transmitted on the BSC with the error probability , whereas the check symbols on the noiseless channel, then the average error probability of decoding on the ensemble of all -codes meets the following modified Gallager’s bound

| , | (11) |
| --- | --- |

where

| , | (12) |
| --- | --- |
|  | (13) |

is Gallager’s function for BSC with the error probability

|  | (14) |
| --- | --- |

is the code rate. We note that in the frame of the above model, the code rate  satisfies the inequality

| , | (15) |
| --- | --- |

where  is the capacity of the BSC with the probability of error .

It follows from (15) that . In the asymptotic case , then

| . | (16) |
| --- | --- |

We see from (16) that an arbitrary small value of the erroneous decoding probability is achieved for large block length if the number r of check symbols (but not block length) is proportional to the number of information symbols k with coefficient .

D. Authentication based on the class of universal hash functions

In order to execute the authentication procedure, we use the universal hash function which are described below.

For any finite set A, let \A\ denote its cardinality. For any two finite sets A, B, let H be a set of hash-maps A B. For each x0, x1 A, let  be the number of hash functions in H that collide in x0 and x1. We recall that H is universal2, U2 in short, if for each x0, x1 A, .

Let Pcol be the so called collision probability, namely the probability that there occurs a pair of elements in A colliding under an uniformly chosen map h  H. Clearly, Pcol  . The class H is strongly universal2, SU2, if

(16a)

and besides for each distinct x0, x1 A, and each y0, y1 B,

For a given , the class H is ε-almost universal,  ε -AU2, if for all x0, x1 A: . The class H is  ε -almost strongly universal, ε -ASU2, if (16a) holds and for all  x0, x1 A, and all y0, y1 B, . Naturally, each class  -ASU   is also SU2.

Examples of hash functions classes: We assume that the sets A and В consist of all binary sequences of lengths a and b, respectively: A = {0,1}а, В = {0,1}b, hence |A| = 2a, |B| = 2b.

An U2 class. The set A can be identified with the Galois field GF(2a). For each s GF(2a), let hs : A  В,   , where the map  takes the b least significant bits in z. The class  is U2. Such hash functions are described uniquely by binary strings of length a.

An SU2 class. For each s,t  GF(2a), let hst : A  A, x  sx + t. The class  is SU2 and clearly this class can be indexed by sequences of length 2a.

An ε-SU2 class. It has been shown in [31] that the hash functions chosen from an ε -SU2 class are connected with incomplete balanced schemes. The parameters of the ε-SU2 class can be

described as follows

| , | (17) |
| --- | --- |

where q is a power of a prime and  is an integer.

Let us analyze the procedure of message authentication. Let x be the message to be authenticated during its transmission from user A to user B. User A forms the authenticator  of his message x using the keyed hash function known by him (but unknown for adversary E), then A appends y to x and sends the pair to the legal user B. In order to check the authenticity of the message x, the user B receives a pair (which may be forged), B  forms authenticator  with his knowledge of secret hash function h and compares  with . If they coincide then B accepts x, otherwise he rejects it.

It was shown in [31] that if the hash functions, chosen from the  class, are used in the authentication procedure then for the best adversary’s strategy consisting in an impersonation or substitution of the messages, the following probability bounds hold

| , | (18) |
| --- | --- |
| , | (19) |

where is the probability of message impersonation, and is the probability of message substitution.

Let us define the probability of undetected false message deception by the adversary as. The bounds (18), (19) will hold only if the active adversary ignores completely the used hash function h in the authentication procedure. But there may be situations when the keyed hash function is partly known by the adversary although authentication procedure is still possible. In order to clarify this situation let us recall  initially from [18] that for a discrete random variable taking values over a set X with probability distribution  the minimal entropy is

| , | (20) |
| --- | --- |

and the Renyi entropy of the random variable X is

| . | (21) |
| --- | --- |

Theorem 3 [38]: Suppose legal users A and B have the random key h with length l0 within an authentication scheme based on ε -SU2 hash functions where ε = . Denote by U the total knowledge of E about h. Then, assuming that for any sample u

,       0 < t < 1,                                                (21a)

the probability Pd of message undetected deception is upper bounded as

.                                                           (22)

### Authentication based on noisy channels

The message authentication considered above and based on the use of hash functions from either the class  or the class  requires a possession by legal users of the secret or partly secret keys. However such keys cannot be taken directly from the strings ,  shared in the initialization phase because they differ even for legal users. On the other hand it is impossible to conciliate these string by sending from A to B the check symbols strings of  because PDC is get not authenticated and B could “conciliate” formerly the false string  with E.

In order to avoid this situation it is necessary firstly to design a keyless message authentication based on noisy channels. In [16] a special type of codes has been proposed in order to solve this problem: the so called  authentication codes (AC). Let us describe them briefly.

In an initialization phase the users share the strings ,  over a BSC () and they agree an error correcting binary systematic -code V in order to authenticate a length  message. The authenticator  of a message m is formed as follows: for each i  let  be the i-th bit of the codeword in V corresponding to m and if , or let it undefined otherwise.

After receiving a pair  user B forms his authenticator  for the message  using his string  according to the agreed procedure and compares  with . If the number of the coinciding bits in them is less or equal to some given threshold  then message  succeeds as authentic, otherwise it is removed as forged. The AC’s were investigated in [16] and can be characterized by two probabilities:

– the probability of false removal of the message although adversary E does not intervene at all;

– the probability of the deception of false message, i.e. the probability of the event that E is a forged message and this fact was not detected by B.

,  do not depend on ordinary minimum code distance of the code V but on the so called minimum asymmetric semidistance  that is determined by the minimal number of differences between 0 and 1 symbols in any pair of distinct code words of V.

Theorem 4 [26, 32]: Let V be an -AC with constant Hamming weight τ for all non-zero codewords and with asymmetric semidistance . Then the probabilities ,  for authentication procedure on noisy wire-tap channel with parameters , can be upper bounded as follows:

| , | (23) |
| --- | --- |
| . | (24) |

It is a very hard problem to find  for any linear code. But there exists a very simple method to design the code V with known , given the linear -code  with known ordinary minimum code distance d proposed in [16].

Namely, let us substitute the symbol 1 with the symbol pair 10 and the symbol 0 with 01 in .Then evidently the parameters of the code V are:

|  | (25) |
| --- | --- |

We have proved in [26] the following theorem with the use of the code above.

Theorem 5: Let V be a -error correction code with minimum distance that is used in the authentication procedure. Then for any  there exists an integer  and an AC, guaranteeing   for all .

It follows from this theorem that

as .                                                                                        (26)

This means that the length of the authenticator approaches zero as the block length tends to infinity. Other methods to design constant weight AC were investigated in [33].

F. Extractors

Let us recall the notion of extractor and  strong extractor [35]-[37].

Two probability distributions P, Q, defined on the same set X, are called ε-close if their statistical difference

|  | (26) |
| --- | --- |

does not exceed  ε.

A map is an -extractor if for any probability distribution variable X on such that  and any uniform distribution variable on the statistical difference probability distribution of extractor output to an uniform distribution on is at most ε.

In order words, the extractor maps a random sequence X of length k with symbols taken from ensemble of min entropy  to random sequence of length l that is ε-close to uniformly distributed sequence with the help of truly random sequence of length u. The last sequence can be seen as a “seed” of the extractor.

The extractor E(X, Г) has parameters (k, , u, l, ε), where k is the length of input random sequence,  is the evaluation of min entropy () on the set of input sequences, u is the length  of the seed γ, l is the length of the output sequence, ε is the statistical distance between the output probability distribution and the uniform distribution on the output set.

A mapping is called a strong extractor  if for any probability  distribution random  variable X on the set having minimal entropy   and for any uniform distributed random variable  on the set  the probability distribution of the concatenated variables (() is close to an uniform distribution on . More specifically

.                                               (27)

This means that the strong extractor provides the closeness of probability distribution for the concatenation of the output extractor sequence and the seed sequence to an uniform distribution. In the current paper we will consider only extractors based on the construction proposed by Trevisan [38] and improved in [36], [37].

Theorem 6. (See theorem 22 in [36]). For every k,  , N and ε > 0, such that l ≤ ≤ k, there are explicit strong (,ε)-extractors with

,                                                                          (28)

or

,                              (29)

where 1+ μ= k/(l-1), μ < 1/2 and Δ=O(d).

The value Δ is the loss of extractor output sequence length.

The first extractor (28), with  constant, is used for extraction of an arbitrary part of randomness () from input sequence Xk , whereas the second one (29) is needed in order to extract all randomness   l= from input sequence Xk.

We are not going to use the estimates based on the O-operator and therefore let us find a more accurate estimate for the length of the seed. For this reason we consider in greater detail the design of the Trevisan’s extractor modified by Raz, Reingold, Vadhan [36].

In order to design the Trevisan’s extractor it is necessary to realize three components:

- The linear error code W: With parameters  and minimal code distance dw, where ,ν- integer. It is proposed to take this code as a concatenation of the Reed-Solomon and the Adamar codes.

2. Combinatorial block design scheme. (Balance incomplete block design, BIBD). This is a family of sets S = {S1, S2, … Sl} holding the following properties:

| , | (30) |
| --- | --- |
| , | (31) |
| for , where . | (32) |

This means that the family consists of l sets or blocks, each consisting of ν elements taken from the set of integer {1,2,…,u}, while the number of elements contained simultaneously in any pair of blocks is at most . Such construction is designated as a (v, с)-scheme.

3. Boolean function f from ν arguments , for which the following relation holds: , where is a codeword of the code W.

The design of extractor based on three components given above is presented in fig.2.

Fig 2. Design of Trevisan’s extractor

The algorithm is executed in the following stages:

- The input sequence is encoded to with the error correcting -code W. The word  gives the value of the Boolean function .

- Random sequence γ of length u determines the samples γ|Si, consisting of ν symbols of γ with the use of blocks Si belonging to the (ν,c)-BIBD. This means   ,  .

- The l  values  of Boolean function f for arguments γ|Si , e.g. wi = f(|Si) i=1,2,…,l are found. The l values are the output of extractor.

In the modified extractor version [36] it was proposed to use a (ν,c)-week scheme, in which the condition (32) is changed to the condition

| , | (33) |
| --- | --- |

where с is some constant (с>1).

The W-code length  is chosen in [36, p.106] according to the condition

| , | (34) |
| --- | --- |

Since w is the output of Boolean function with v arguments, should be equal to. Obviously this condition will be fulfilled if

| , | (35) |
| --- | --- |

where  is the “ceiling” of x (the least integer greater or equal than x).

The characterization of strong extractor is determined by the following statements.

Theorem 7 (Proposition 10 in [36]). If S ={S1,…,Sl } (with) is a weak (v,c)-design for

(36)

then  is a strong  -extractor.

Theorem 8 (Lemma 15 in [36]).  For every v,lN and c>1, there exists a weak (v,c)-design S ={S1,…,Sl}  () with

| . | (37) |
| --- | --- |

Moreover, such a family can be found in polynomial time poly(l,u).

Theorem 9 (Lemma 17 in [36]).  For every v,l N and , there exists a weak (v,1+μ)-design S ={S1,…,Sl}  ( ) with

| . | (38) |
| --- | --- |

Moreover, these families can be found in time poly(l,u).

The results of Theorem 6 will be avoided in our further investigation because a presentation of the output sequence length u in the form  is inconvenient in the optimization procedure.

We will get an estimate of u taken from the results of Theorems 7-9 directly. More specifically, using (35) and (37) one can write the relation for the necessary number of seed symbols for the first extractor (28) in Theorem 6.

| . | (39) |
| --- | --- |

For the second extractor (29), it follows from the proof of lemma 17 in [36] that , where  , , . Then in terms of (37) we get

| . | (40) |
| --- | --- |

### G. Privacy amplification

The procedure of privacy amplification (PA) at the final stage of the key generation between users A and B has been investigated in detail in [14,21]. PA can be implemented either by hashing [14,21] or by extraction [31]. We will consider in the current paper the second approach.

In order to compare our new results with the results obtained in [26] where hashing has been used as the privacy amplification procedure, let us specify an application of both methods.

The sequence  of length k bits is mapped by the user A to the sequence  of length l through a keyless hash function from the class , or . In a similar manner the user B forms his key  after error-correcting his sequence .

The most important parameter of the PA procedure is the residual Shannon’s information received by the adversary E, concerning the final key . The estimates of this information leaking of E are given in [14,21] for different settings of wire-tap channels. The more general bound is presented below.

Theorem 11 [14]: Let  be the sequence of length k transmitted from A to B over a BSC with the error probability  and received by B as the sequence . Assume also that  is the result of receiving  by the adversary E over a BSC with probability , while the Renyi information contained in  about  is t. Let H be a -class of hash functions from {0,1}k into{0,1}, known by all participants (A, B and E) and let  be truly randomly hash function chosen by A, transmitted to B over a PDC. If the users A and B compute their keys as , , then the amount of Shannon’s information about the keys , is upper bounded by

| . | (41) |
| --- | --- |

The Renyi information t is connected with Renyi entropy  as follows

| . | (42) |
| --- | --- |

For the BSC used as wire-tap channel we have by (21)

| . | (43) |
| --- | --- |

If the adversary receives some extra information about  aside the information contained in  (for instance the sequence  of check symbols of length r eavesdropped by E over the PDC), then the amount of conditional Renyi entropy  that received E can be estimated by the theorem 12.

(This theorem also gives the estimation of the amount of conditional minimal entropy  which we use later).

Theorem 12 [21]: Let X and C be two random variables and let . Then the following inequalities hold

| . | (44) |
| --- | --- |

with the probability at least ,

|  | (45) |
| --- | --- |

with the probability at least .

We can apply (44) in order to estimate . Then we get

| . | (46) |
| --- | --- |

It follows from (42) and (46) that

| . | (47) |
| --- | --- |

Substituting from (47) into (41) instead of t, we get the upper bound of Shannon’s information leaking to E

| , | (48) |
| --- | --- |

that holds with the probability

| . | (49) |
| --- | --- |

In order to compare the performance of privacy amplification based on hashing and on extraction, let us prove a new lemma establishing a connection between the Shannon’s information leaking to adversary regarding the key at the output of the extractor, and the statistical difference  among distribution of the final key and an uniform distribution.

Lemma 1. If the statistical distance between the output of the extractor generating the length  key and an uniform distribution is at most , then the amount of the Shannon(s information concerning the key got by any adversary is upperly bounded by

.                                                                         (50)

Proof. The following inequality holds by definition of strong extractor

| , | (51) |
| --- | --- |

The meaning of this inequality is that the probability distribution of the extractor’s output and the “seed”  concatenation is close enough to an uniform distribution.

We note initially  that for an uniform distribution on the space , the following equality holds

|  | (52) |
| --- | --- |

where  is a random sequence, Гu is the probability distribution of ,  is the expectation with respect to the distribution Гu, and Е(.) is an abbreviation of the notion Ext(.).

In fact, the left side of (52) is expressed as:

| . | (53) |
| --- | --- |

Since the distributions and  are both uniform, the right side of (53) is transformed as:

| , |  |
| --- | --- |

proving (52).

By combining (51) and (52) it is obtained

| . | (54) |
| --- | --- |

Using the well known Markov’s inequality, (54) implies

| , | (55) |
| --- | --- |

where  is some arbitrary value.

An inequality has been proved in [21, lemma 6], which in our notation is

| . | (56) |
| --- | --- |

Taking into account that the output extractor sequence is just the key, we can write

| . | (57) |
| --- | --- |

Then by substituting (57) into (55) it is obtained

| . | (58) |
| --- | --- |

It follows from (58) a trivial estimate for the averaged value  over, namely

| . | (59) |
| --- | --- |

After a simplification on the right side of (59) and by neglecting smaller values than 2-l,

| . | (60) |
| --- | --- |

Then for the amount of information leaking of an adversary concerning the key , given the knowledge of  , the following bound is obtained

| . | (61) |
| --- | --- |

The right side of (61) is minimized under  giving the final inequality

| . |  |
| --- | --- |

providing thus the desired result.                                                                                    ■

It follows from the above lemma that if the value of the statistical difference at the extractor output that forms the length l key does not exceed ε, then the amount of the residual information regarding the key obtained by the adversary does not exceed .

This means that a requirement, regarding the amount of Shannon’s information on the key leaking to an adversary, of the form  will be fulfilled whenever . This fact results in the following requirement to the extractor’s statistical distance:

.                                             (62)

III. Key distribution protocols

Two key distribution protocols in presence of an active adversary have been proposed by Maurer and Wolf in [21]: the UH-protocol, in which privacy amplification procedure was executed using hash functions and the EX- protocol in which this procedure was based on extractions. It has been shown in [21] that the EX- protocol majors the UH-protocol with respect to several conditions.

We want to investigate a performance of these and other new protocols. We will show that our new protocols are superior than those considered in [21] for non-asymptotic cases (e.g. when lengths of the sequences are finite).

Initially we consider modified UH and EX- protocols and denote them as α- and αext -, respectively. A difference between the original and the modified protocols is determined by two factors.

- We consider protocols under the condition,  or equivalently the conditions ,. This requires to send the check symbols from A to B in order to conciliate Хk and Yk.

- Instead of the authentication algorithm “request-response” presented in [21], we will use non-interactive the AC-based algorithm (see Section II) because this allows the users to provide authentication even when the sequences Хk and Yk do not coincide completely. By the same reason, the authentication algorithm and the number of substrings of the original strings Хk and Yk  are changed.

Before the execution of the α-, αext-protocols, the users A and B divide their respective sequences Хk, Yk, into and  of lengths k1, k2. (The first parts  and  will be used for key generation in the execution of the PA procedure while the second parts  and  will be used in the execution of the authentication procedure).

Since the α –protocol was already considered in [26], we move on to the αext –protocol.

- The user А forms the string  of check symbols  of length r1 to the string using a (k1+r1, k1)–error correcting code С1. (This code should be agreed by users in advance.)

- The user A generates a truly random binary sequence  (which will be used as an extractor seed) of length u.

- The user А forms the authenticator w for the message  using for that an AC based on error correcting (n0, k0 = r1+u, d)- code and the sequence.

- The user А sends to В the message  over a PDC appended with the authenticator w.

- The user В verifies the authenticity of the message  through the known (n0, k0)-AC and his string (see section II.E). If authenticity is confirmed, then B goes to the next step. Otherwise he rejects the KDP.

- The user В corrects the error in string  through the check symbols string . We denote by  the string  after error correction.

7.	In order to get the keys  and both users A and B execute a privacy amplification procedure based on an extractor (see section II.F): ,.

Recall that the α –protocol differs from the αext –protocol in that it generates a hash-function h in step 2.  This hash-function jointly with the check symbols of C1 and the authenticator w are transmitted to B (steps 3-5). In the seventh step this hash-function is needed for key generation:, .

It has also been proposed in [26] a new β-protocol that differs from the α-protocol in the following:  After the execution of the initialization phase, both users A and B have got the strings that can in fact be used to form the hash functions. In this way, we do not require to send the hash functions over the PDC, hence the length  used before for authentication of the hash function can be shortened. Therefore we may expect that the length of substring is increased (if the total length of the string X is fixed). But such conclusion is not so apparent because we have to extract the hash function as a segment from the string X.

A similar problem appears in the case in which an extractor is used instead of a hash-function for privacy amplification. In the αext –protocol A generates a truly random sequence  and sends it to B jointly with the authenticator of . But the required sequence  can be gotten directly by both users A and B from the initially distributed strings X and Y. This results in the following βext -protocol.

It is worth to note that although  is not uniformly distributed from the adversary’s point of view this has no relevance for strong extractors.

In the above setup, users A and B divide the strings Хk, Yk into three disjoint parts ,,and , , , with  k1 + k2 + k3 = k.  Then they execute the following steps:

- The user A forms the length r1 string  of check symbols of the string  using the error correcting -code С1, agreed in advance.

- The user A forms the length r2 check string  of the string using the error correcting -code С2, agreed in advance.

- The user A forms the authenticator w of the message  using an AC and his substring .

- The user A sends to B the message  over a PDC appended with w.

- The user B verifies the authenticity of the message  using a AC and his substring . If it is confirmed then he goes to the next step. Otherwise he rejects the KDP.

- The user B corrects errors on strings ,  using the check strings  and . Denote by ,  the strings , after error corrections.

- The users A and B take their substrings , , where k3=u, as the second arguments in their extractors.

- Both users A and B form the keys as ,.

Performance evaluation of protocols

A theorem has been proved in [26] determining the optimal parameters for both the  α-, and β-protocols depending on the posed requirements. Let us prove a generalization of that theorem for the α-, β-, αext -, and βext-protocols. We will assume that for the  α-, and β-protocols a hashing is used as privacy amplification procedure, whereas for αext -, and βext-protocols an extraction is used. Moreover we assume that the first extraction scheme considered in section II.F is used, where the number of random bits u is determined by equation (39).

Theorem 10: Let us assume that the users A, B and the adversary E have binary strings Xk, Yk and Zk, respectively after execution of the initialization phase over the wire-tape channel, , , ,. Then A and B are able to form a common key of length l satisfying the requirements (3)-(7) after the execution of any of the α-, β-, αext -, and βext-protocols if the parts of lengths  on which were divided the substrings Xk, Yk for the α-, and αext -protocols or the parts of lengths  on which were divided the substrings Xk, Yk for the β-, and βext-protocols satisfy the equations listed below:

| , | (63) |
| --- | --- |
| , | (64) (65) |
| whereand are determined by (11)-(14) and , is the number of the extractor random symbols, c is a parameter under optimization, | (66) |
| , | (67) |
|  | (68) |
| , | (69) |
| where |  |
| , | (70) |

and r2 being the number of check symbols of the error correcting -code found similarly as in eq's (63),

| . | (71) |
| --- | --- |

The key rate is then determined as follows:

| ,, | (72) |
| --- | --- |
| , . | (73) |

Proof.

For the α- and β-protocols the theorem has been proved in [26]. Let us prove it only for the αext- and βext -protocols.

Let the bounds of the KDP parameters meet exactly all requirements (3)-(7), e.g. the following equation hold:

| , | (74) |
| --- | --- |

where   is the code rate, andis computed by (11) - (13). Under the condition that the adversary gets the sequence  over a BSC with error probability  the conditional minimal  entropy is

=.

Since the adversary receives also the check block , in line with (45) the following inequality results:

| , | (75) |
| --- | --- |

which does not comply with the probability . A substitution of (75) into (36) and a terms rearrangement gives

.                                                                                (76 )

The value u in (76) is the number of the extractor random symbols. In order to find it, we can use (39) substituting ε by   in line with Lemma 1 that results in (66). Next, using again Lemma 1 and assuming , we obtain (65) by (76). A solution of the equation system (63) and (65) allows to find the parameters k1,r1, given a fixed c. It will be shown in the sequel that the key rate can be maximized by a proper selection of the parameter с.

In order to find  let us assume that the probabilities Pf and Pd have equal values.

|  | (77) |
| --- | --- |
|  | (78) |

where  are the parameters of error correcting codes used in the AC.

Recall that for the AC we had where  is the length of the error correcting ()-code with minimum distance d. For the αext-protocol , while for the βext-protocol , where   is the number of check symbols in the -code C2. This gives relation (70) for the parameter .

Using the Varshamov-Gilbert inequality connecting  and taking into account that  we get

.                                                                                          (79)

Solving the equation system (77)-(79), equivalent to the equation system (67)-(69), we find the parameters k2, d.  The value r2 is calculated by (11)-(13), in which it is necessary to let, .

In line with the above protocols, we have that for the αext-protocol,  and for the βext –protocol, . This fact proves (71).

Then relation (73)  is apparent from the protocols description.		■

Remark 1. If the solution of system (63)-(71) is not unique then it is reasonable to select any of them maximizing the key rate.

Remark 2. It is worth to note that the values ,c found for the same requirements , but for different protocols, may be different.

Remark 3. (Choice of the coefficient c in (65), (66)). In Fig’s. 2, 3 the dependence of the key rate for the αext -protocol and the  βext-protocol is plotted versus the parameter c, given fixed values l for different error probabilities  in the main channels.

Fig.2 Dependence of key rate versus the parameter extractor c for αext -protocol

Fig. 3. Dependence of key rate versus the parameter extractor c for βext -protocol

We assume that pw = 0.2,  in a plotting of these curves. From these curves it is patent that the key rate depends essentially on the choice of the parameter c.

Let us compare the-, -, αext -, βext -protocols on the key rates.

Theorem 11: If the key length is given and the rate  of the error correction code satisfies, then , and

Proof. The first inequality is proved in  [26, theorem 10]. Let us prove the second inequality. Let us write  and . For a fixed common length, , we should prove .

Under the requirements (2), (3), (7) posed by the KDP parameters, it follows from (64) that l' = l whenever k1 = k’1 and r1 =.Therefore it is necessary just to prove

(79a)

According to the scheme of the AC-code design we can write , where r0    is the number of check symbols of the (n0,k0)-code. , where r’2    is the number of check symbols of the (u+r’2, r’2)-code C2, and r’0  is the number of check symbols of the (n’0,k’0)-code. By substituting the expressions for k2, k’2 presented above into  (79a), we get the equivalent inequality . In order to prove this inequality it is sufficient to show that  and .

The first inequality holds because under the theorem’s condition,  for the (u+r’2, r’2)-code. In order to prove the second inequality, we note that r0 is the number of check symbols of the information block of length  and r’0 is the number of check symbols of the information block of length . It is clear that  and it is followed from Varshamov- Gilbert inequality that  maintains a constant value as the information block length increases in order to get the required error correction capability. Therefore  and this completes the proof of the theorem.                               ■

With the purpose of comparing the protocols performance with hashing and with extraction, let us find the relation of key rate for sufficiently large l.

Theorem 12. As the key length , then the following relations hold

,                                                                                                         (80)

,                                                                                                        (81)

.                                                                                           (82)

Proof.

The proofs of (80) and  (81) were presented in [26]. In order to prove (82), let us write the relations of the key rates at the- and  -protocols  taking into account (73), (25), (70), (71):

,                                         (83)

,     (84)

where u is the length of the extractor seed, r1 is the length of the check string for the ()- code,  r2 is the length of the check symbols string for the ()-code, and r0  is the length of the check string for the AC-code.

According to (16), = for sufficiently large l (and hence sufficiently large k). Let us rewrite (83), (84) as

,                                                                                           (85)

.                                                                                          (86)

A substitution of  given by (65) into (85) gives

,                                                            (87)

or

.                                                 (88)

It is not hard to show that

as .                                                               (88a)

Also theorem 5 establishes that , but since  as long as  according to (65) and (70) we get  .

Because we can write (82) as

,  which approach  maximum as.

And this implies proving (82) for the -protocol.

By substituting (65) into (86) we get

.                                               (89)

Taking into account the used arguments in the proof of (82) for the -protocol, we can see that (82) holds also for the - protocol.                                                                             ■

The following trivial corollary results from the above theorem.

Corollary 1. If the channel parameters and  are such that

(90)

and

,                                                                         (91)

then and  respectively for sufficiently large l.

Corollary 2. If , then  and .

Proof.

If , then the relations (90), (91) can be written as

and                                                                             (92)

Since  [18], then  and .                                         ■

Let us exemplify the above results and illustrate that the -, and -protocols major the -, and -protocols respectively. Let us select the following natural requirements for the KDP:

| Iadm = , Pd = Pe = Pf = Prisk = | (93) |
| --- | --- |

In Fig. 4 we plot the key rates versus its length l for both -, and -protocols with pm = 0.01 and 0.001, pw = 0.2, and the requirements presented in (93).

The optimization of  с has been performed for every value of l. For comparison purposes the dependences and are shown also in the figure.

Fig. 4. The key rates versus their lengths for different requirements imposed to KDPs.

The following conclusions are drawn after an examination of the obtained dependence.

The protocols using extractors have greater key rate than the α- and β-protocols under sufficiently large l and small pm. It is worth to note that if for the α- and β-protocols the asymptotically possible value key rate calculated by (80), (81) can be achieved even in the considered key length range, it is not true for the αext- and βext-protocols, demonstrating a noticeable increasing proliferation of the key rate outside this range.

We can see that the αext- is superior than the α- protocol when  with pm=0.01 and the βext- protocol is superior than the β - protocol when and pm=0.001 (under the stated requirements in our investigations). The key length for which the αext- and βext-protocols are superior than the α- and β-protocols essentially depends on the error probabilities in the communication channels.

The βext- protocol is superior than the  αext -protocol, although these protocols have the same asymptotic key rate. Hence, protocols with extractors are superior than the protocols with hashing, when .

IV. Key distribution protocols under the condition that legal users shared short authentication key before starting the KDP

The α'- and β'-protocols have been introduced in [26], which differ from the α- and β-protocols in that legal users A and B have got short keyof length l0 before starting the KDP. This key can be used for authentication of messages transmitted over public discussion channels in order to get finally the key of length l>>l0.

In this section we consider some modification of the α'- and β'-protocols in which instead of hash functions, extractors are used in order to generate the final key. We call these protocols the α΄ext- and β΄ext-protocols, respectively.

α΄ext – protocol

Let us suppose that the users A and B have binary strings Xk, Yk respectively.

- The user A calculates the check string of length r for the string  using an error correcting (k+r, k)-code C that should be agreed between the legal users in advance.

- The user A generates a random binary string γu of length u.

- The user A computes the authenticator w for the message  using a keyed hash function from the ε-ASU2 class, and the key SA.

- The user А sends to user B the message  appending to it the authenticator w over a PDC.

- The user B verifies the authenticity of  using the algorithm presented in section II. If the authenticity of  is confirmed, then B goes to the next step, otherwise he rejects it.

- The user B corrects errors in the string  using the check string . (We denote by  the string Yk after error correction).

- Both users A and B compute their keys as

β΄ext – protocol

In a similar manner there is a modified -protocol where the random string is not transmitted over the PDC but it is formed from the random sequences Хk, Yk.

The users A and B divide each of the strings Xk, Yk obtained after execution of the initialization phase into two disjoint substrings ,  ; ,respectively. Then they perform the following steps:

- The user A calculates the check string  of length r1 for the substring  using an error correcting (k1+r1, k1)-code С1.

- The user A calculates the check string  of length r2 for the substring  using an error correcting (k2+r2, k2)-code С2.

- The user A forms the authenticator w for the message , using a keyed hash function from the class ε-ASU2 and the key SA with length l0.

- The user A sends to B the message  appended with the authenticator w.

- The user B verifies the authenticity of the message  using the authentication algorithm (see section II) and the key SB. If authenticity is confirmed, then user B goes to the next step, otherwise he rejects the KDP.

- The user B corrects errors in the strings,, using the check strings  and  . (We denote by ,  the strings ,after error correction).

- The user A takes the string  as seed  and the user B takes the string  as seed .

- Both users A and B compute their keys as .

Let us estimate the key rate of these protocols.

Theorem 13: Let us suppose that the users A, B and the adversary E have binary strings Xk, Yk and Zk, respectively after execution of the initialization phase over the wire-tape channel, , , ,. We assume that the users A and B share initially a short key S of length l0 in order to authenticate messages transmitted over the PDC.

Then A and B are able to form a common key of length l satisfying the requirements (3)-(7) after execution of the α΄ext- and β΄ext-protocols if the lengths  of substrings Xk, Yk and Zk, and satisfy the equations listed below:

| , | (94) |
| --- | --- |
| , | (95) |
| whereand are calculated by (13)- (15) and , | (96) |
| , is the number of the extractor random symbols and c is the parameter under optimization, | (97) |
| , | (98) |
| , | (99) |
| where |  |
|  | (100) |

and r2 being the number of check symbols of the error correcting -code found similarly as in eq's (94)-( 95). The key rate is then determined as:

| ,. | (101) |
| --- | --- |

Proof.

The relations (94), (95) and (97) can be proved similarly as (63), (64) and (65) in theorem 10. The relation (96) is apparent from the protocols description. In order to prove (98), (99) we assume that for authentication of messages of length a (see relation (100)) an-ASU2–hash-function is used. Relying on (17) we write . Let us put , then

.                                                                     (102)

Let us assume that the probability of false message deception is equal to . Then  from (102), relations (98), (99) are true. The relation (101) follows from the protocols definition taking into account that the number of the extractor random bits can be optimized with respect to the parameters c. By substituting (95) into (101) we get that as , then

,                                                           (103)

.                                                       (104)

From (103), (104), we have . When  both protocols have the same key rates

.                                                                              (105)

Let us compare the key rates of the α΄ext- and β΄ext-protocols and  the α’- and β’-protocols. In [26] the following relations have been proved: and  as . Comparing these relations with (105) we may conclude that for any values  and .  can be either large or smaller than  depending on the ratio of  and .

In order to illustrate the above assertions we plot in Fig. 5 the dependence of the key rate versus its length for the α'-, β'-, α΄ext - and  β΄ext-protocols, given pw = 0.2,  and Iadm = , .

# Fig.5. Key rates versus its length for different KDP provided initially with short authentication keys

V. Two-stage (hybrid) protocols with extractors

We remember that the hybrid protocols [26,38] are combinations of protocol pairs , , ,  where the first protocol in the pair is used in order to generate relatively short key S of length l0 required for hash function and check bits authentication, whereas the second protocol is used in order to form the final key K.

The keys S and K can be obtained by execution of the privacy amplification procedure based either on the use of hash functions or extractors. This means that for every above mentioned hybrid protocols, there are four variants of hashing or extracting applications. In total, there can be formed 16 protocols, which in turn can be split into four groups as shown in Table 1.

Table 1.  Groups of hybrid protocols

| Groups of protocols | - or -protocols for generating authentication key | - or -protocols for key generation |
| --- | --- | --- |
| 1 | ,,, | hashing | hashing |
| 2 | ,,, | hashing | extracting |
| 3 | ,,, | extracting | hashing |
| 4 | ,,, | extracting | extracting |

The first group of protocols was investigated in [26], and there it has been proved that every such protocol can be the most efficient depending on the additional key requirements imposed to it. It is worth to note that even for large length of key K, the length l0 of the authentication key occurs moderate [26], p. 2543. If =32000 (pm = 0.01, pw = 0.2, ),   then l0 = 678. But since, as shown in section III, extractors are superior than hash functions only with large key lengths, their application is useless in the first stage of the hybrid protocols, where a short key is required.

Therefore, the protocols from groups 3 and 4 have not been considered. It is sufficient to investigate protocols from the second group, where the authentication key is generated by hashing and the generation of the final keys is performed by extraction. Thus we consider the following hybrid protocols: (α, ), (α, ), (β, ) and (β, ). For a more detailed description with the design of these protocols and the specification requirements of each protocol component, we refer to [26, p. 2544].

Let us give a short description of the (α, α΄ext)-protocol. It is based on the (α, )-protocol proposed by Korzhik and Morales [38]. In this protocol, the sequences Хk, Yk of users A and B are divided into three parts , , and , , , respectively (see Fig. 6a). Subsequences ,  (, ) are used for the generation of the authentication keys SA (SВ). Subsequences () and keys SA (SВ) are used in the -protocol for final key КА (КВ) generation. The key rate of this protocol can be written as

| , | (106) |
| --- | --- |

where  is the key S rate at the length l0 in the α-protocol.

Let us prove the following lemma.

Lemma 3. The convergence , as , holds in the (α, ) -protocol.

Proof. Let us consider the (α, α΄ext)-protocol. According to (100) the input block length of the ε-ASU2 hash-function used in the α΄ext-protocol is equal to . We show initially that  as . The relations (97) and (14) give

,                                                                                                       (106a)

.                                                                                                               (106b)

Thus in order to prove that  it is necessary to show that  as . Taking into account equation (16), we can present (64) in the form

.                                                       (107)

Fig 6. Different types of hybrid protocol with extractors

From the above relation, it follows that  as  and (106b) and (106a) result as  and . Then using (98) for an estimation of hash function parameters we may write

| . | (108) |
| --- | --- |

Using (107), (106) can be expressed as

| . | (109) |
| --- | --- |

Taking into account that  is constant and (see Lemma 3) we can see that the last term in the denominator of (109) approaches to zero as . Other terms in the denominator of (109) also approach to zero because they consist either of values approaching zero or have a logarithmic dependence on l.

Because approach maximum as, then the following asymptotic estimation holds for the key rate of the (α, )-protocol

| . | (110) |
| --- | --- |

, as pm → 0.

In the (β, α΄ext)-protocol (see Fig. 6b) the sequences Xk, Yk are divided into four parts , ,, and ,,,, respectively. The subsequences ,, and ,,are used in the β-protocol in order to generate the authentication key S of length l0. The subsequence () is used in the -protocol for final keys KA, KB generation. One can write

| , | (111) |
| --- | --- |

where  is the authentication key rate.

By comparing this protocol with the previous one, we can conclude that for the same length of the final key, the equality should hold. As it was shown in [26],  and the length  of authentication key for the -protocol is larger than the length  of the authentication key for the -protocol. Hence  and .

It is easy to show that

| , | (112) |
| --- | --- |

as , that coincides with the key rate of the (α, )-protocol (see (110)). If pm = 0  we get by (112)

| . | (113) |
| --- | --- |

Next let us consider the (α, β΄ext)-protocol (see Fig. 6c) in which each sequence Xk, Yk is divided into four parts  and  respectively. Subsequences  and  are used in the α- protocol for the generation of the key SA, or SB for the -protocol, while subsequences  and  are used in the -protocol for the final key KA (KB) generation assuming  and  as random “seeds”  while using in extractor.

Similarly to (106) we can write

| . | (114) |
| --- | --- |

The parameter l0 is smaller in this protocol than in the (α, )-protocol, because only to authenticate the check sequences  and of total length (r1 + r2) there is used an ε-ASU2 hash-function. However additional item (u) calculated by (66) increases the denominator and hence .

In the (β, β΄ext)-protocol, each sequence Xk, Yk of users A and B is divided into five parts ,,,and ,,,,, respectively (see Fig 6d). Subsequences ,, and ,, are used in the β-protocol to generate the keys SA, SB. Subsequences ,and , are used in the -protocol to generate the keys KA, KB. Let us write

| . | (115) |
| --- | --- |

In this relation by the same reason mentioned during the analysis of the (α, )-protocol, the value l0 will be smaller than in the (β, )-protocol and the rate Rβ is larger. Therefore the third item is slightly decreasing. However the presence of sufficiently large item u results in a key rate decreasing giving the inequality.

There may be for the (α,), (β,)-protocols some equivalent statement to Lemma 3, e.g. it can be proved that  as . Furthermore, by writing the relations for  and u, from theorem 13 it is very simple to get asymptotically achievable the key rate for the (α,)- and (β,)- protocols.

.                                                                            (116)

Hence, the (β, )-protocol has non-asymptotically the largest key rate among all above considered hybrid protocols.

It is worth to compare this protocol with the (β, )-protocol, that (as shown in [26]) has maximum possible key rate for sufficiently large l among all hybrid protocols using hash functions in the privacy amplification procedure.

For the (β, )-protocol one can write [26]

| , | (117) |
| --- | --- |

By comparing (112) with (117) and taking into account that  we can see that for large l,

From this inequality, it follows that an implementation of extractors for large key length in hybrid protocols  are inefficient.

In Fig. 7 there are plotted the key rates versus its length for hybrid protocols under the conditions pm = 0.01 , pw = 0.2, Iadm = , .

# Fig. 7. The key rates for hybrid protocols

The curves were plotted with the use of the technique proposed in [26]. They clearly demonstrate a behavior of the key rate depending on the key length for different protocols. We can see that - and -protocols have the greatest key rates among all hybrid protocols. The -, -, (α,)-, and (β,)-protocols have approximately equal key rates for large key length and the (α,)- and (β,)-protocols have the least key rate among the above considered hybrid protocols.

# VI. Conclusion

In the current paper, an investigation of key distribution protocols based on noisy channels started in [26] has been continued with such a difference that extractors are used instead of hash-functions in the privacy amplification procedure. The main goal was to prove extractor-based protocols efficiency by the criterion of key rate maximization. The relations are non-asymptotic and constructive because they do not include some uncertain coefficients in notations, in contrast with other papers.

We use the modified Trevisan’s extractor [36, 38] in our paper. It has been proposed new βext- and β΄ext-protocols which differ from those known before [21] because the extractor’s seed is not transmitted over the PDC but, instead, it is generated from random sequences obtained by legal user after the execution of the initialization phase. We proved that the use of extractors in the αext - and βext-protocols increases the rate, in comparison with hashing-based protocols only for very large key length l (typically ) and for some specified values of the error probabilities both in the main and in the wire-tap channels.

It was investigated a performance evaluation of the so called extractor-based hybrid protocols, consisting of two protocols executed in a serial manner where the first protocol in a pair is used for the generation of a relatively short key S of length l0. This key is necessary for authentication of check bits, and a random number (seed) of extractor. The second protocol is used for the final key generation. We prove that extractor based protocols should be used only in the second protocol of the pair.

We selected four hybrid protocols for further investigation (α, )-, (α, )-, (β, )- and (β, )-protocols. The relations for their key rates have been derived for both finite and asymptotically growing key lengths. The greatest key rate is got by the (β, )-protocol. This protocol was compared with the (β, )-protocol considered in [26], which has the greatest key rate among all hybrid hashing-based protocols. The investigations showed that hybrid protocols with the use of extractor-based second stage protocols are less efficient than hashing-based protocol.

We investigated also (but not in a deeper detail) other variants of extractors from [36]. Even with some improvement of their characteristics (in the sense of the seed length), the general conclusion is kept the same: the use of extractors is justified only with very large key length.

We get also asymptotic estimates for the key rates of all proposed protocols that allows to compare the potential efficiency of all considered early protocols. These relations are presented in Table 2.. We can see that asymptotically all hybrid protocols have the same key rates equal to  ,  that is larger than the key rates for single  αext and βext protocols  that is equal to  .

These relations are similar “on structure” to relations for key capacity [23] but differ from the last one in changing of Shannon’s entropy    to min entropy  .

If the main channel is noiseless then all protocols using extractors have the same asymptotic key rates equal to .It is worth to noting that asymptotically all hybrid extractor-based protocols are inferior to hash-based protocols. But this conclusion may be considered as a consequence of crude estimate of information leaking to eavesdropper based on the use of min entropy.

Finally we will present a summary table of key rates for different KDP. It can be seen from Table 2 how closer or farther are the key rates to the secret key capacity given by (9).

Table2

| Protocol type | Non asymptotic relations for key rates | Asymptotic relations for , as l → ∞ | Asymptotic relations for , as l → ∞, pm→ 0 |
| --- | --- | --- | --- |
| αext |  |  |  |
| βext |  |  |  |
| α’ext΄ |  |  |  |
| β’ext |  |  |  |
| (α, α’ext ) |  |  |  |
| (β, α’ext ) |  |  |  |
| (α,β’ext ) |  |  |  |
| (β,β’ext ) |  |  |  |
| where ; formulas for - see (66), for - see [26] |

# References

- E. Knill. Bulding Quantum Computers/ Plenary talk presented at the 2007 IEEE International Symposium on Informational Theory. IEEE Information Theory Society Newsletter. Vol.58, No 4, December 2008, pp. 32-35.

- C. E. Shannon, “Communication theory of secrecy systems.” Bell System Technical Journal, vol. 28, no. 4, pp. 656–715, 1949.

- M. E. Hellman, “An extension of the Shannon theory approach to cryptography.” IEEE Transactions on Information Theory, vol. 23, no. 2, pp. 289–294, 1977.

- C. H. Bennett and g. Brassard, “Quantum cryptography: Public key distribution and coin tossing,” in Proceedings of International Conference on Computers, Systems and Signal Processing, December 1984.

- T. Aono, K. Higuchi, T. Ohira, B. Komiyama, and H. Sasaoka, “Wireless secret key generation exploiting reactance-domain scalar response of multipath fading channels,” IEEE Transactions on Antennas and Propagation, vol. 53, no. 11, pp. 3776–3784, 2005.

- A. Kitaura and H. Sasaoka, “A scheme of private key agreement based on the channel characteristics in OFDM land mobile radio.” Electronics and Communications in Japan (Part III: Fundamental Electronic Science), vol. 88, no. 9, pp. 1–10, 2005.

- H. Mori, H. Sasaoka, and T. Ohira, “Performance estimation of secret key agreement system exploiting an ESPAR antenna and a received signal strength indicator,” in ISSSE2004.    IEICE, 2004.

- H. Imai, K. Kobara, and K. Morozov, “On the possibility of key agreement using variable directional antenna,” in Proc. 1-st Joint Workshop on Information Security, 2006, pp. 1432–1436.

- A. Wyner, “Wire-tap channel concept,” Bell System Technical Journal, vol. 54, pp. 1355–1387, 1975.

- I. Csiszar and J. Korner, “Broadcast channel with confidential messages.” IEEE Transactions on Information Theory, vol. 24, no. 2, pp. 339–348, 1978.

- V. Korjik and V. Yakovlev, “Non-asymptotic estimates for efficiency of code jamming in a wire-tap channel,” Problems of Information Transmission, vol. 17, pp. 223–22, 1981.

- ——, “Capacity of communication channel with inner random coding,”

Problems of Information Transmission, vol. 28, pp. 317–325, 1992.

- R. Ahlswede and i. Csiszar, “Common randomness in information theory and cryptography – part i: Secret sharing,” IEEE Transactions on Information Theory, vol. 39, no. 4, pp. 1121–1132, 1993. [Online]. Available: citeseer.ist.psu.edu/ahlswede93-common.html

- C. H. Bennett, G. Brassard, C. Crepeau, and U. M. Maurer, “Generalized privacy amplification,” IEEE Transactions on Information Theory, vol. 41, no. 6, pp. 1915–1923, 1995.

- U. Maurer, “Secret key agreement by public discussion from common information.” IEEE Transactions on Information Theory, vol. 39, no. 3, pp. 733–742, 1993.

- U. Maurer, “Information-theoretically secure secret-key agreement by not authenticated public discussion,” Lecture Notes in Computer Science, vol. 1233, pp. 209–223, 1997.

- ——, “Protocols for secret key agreement by public discussion based on common information.” in CRYPTO, ser. Lecture Notes in Computer Science, e. f. Brickell, Ed., vol. 740.    Springer, 1992, pp. 461–470.

- U. Maurer and S. Wolf, “Privacy amplification secure against active adversaries,” Lecture Notes in Computer Science, vol. 1294, pp. 307– 321, 1997.

- ——, “Secret-key agreement over unauthenticated public channels I: Definitions and a completeness result.” IEEE Transactions on Information Theory, vol. 49, no. 4, pp. 822–831, 2003.

- ——, “Secret-key agreement over unauthenticated public channels II: the simulatability condition.” IEEE Transactions on Information Theory, vol. 49, no. 4, pp. 832–838, 2003.

- U. Maurer and S. Wolf, “Secret-key agreement over unauthenticated public channels iii: Privacy amplification.” IEEE Transactions on Information Theory, vol. 49, no. 4, pp. 839–851, 2003.

- ——, “Unconditionally secure key agreement and the intrinsic conditional information.” IEEE Transactions on Information Theory, vol. 45, no. 2, pp. 499–514, 1999.

- ——, “Towards characterizing when information-theoretic secret key agreement is possible.” in ASIACRYPT, ser. Lecture Notes in Computer Science, K. Kim and T. Matsumoto, Eds., vol. 1163. Springer, 1996, pp. 196–209.

- V. Korzhik, V. Yakovlev, and A. Sinuk, “Achievability of the key-capacity in a scenario of key sharing by public discussion in the presence of passive eavesdropper,” in MMM-ACNS. Springer Lecture Notes in Computer Science 2776, 2003, pp. 308–315.

- ——, “Key distribution based on noisy channel and error detecting codes,” in Proc. Workshop MMM ACNS 2001. Springer Lecture Notes in Computer Science 2052, 2001, pp. 242–250.

- V. Yakovlev, V. Korzhik, G. Morales-Luna.  Key Distribution Protocols Based on Noisy Channel in Presence of Active Adversary: Conventional and New Versions with Parameter Optimization.  IEEE Transaction on Information Theory. Vol. 54. No 6, June 2008. pp. 2535-2549.

- C.Gehrmann, C.J. Mitchell, K.Nyberg. Manual authentication for wireless devices.

- M. Naor, G.Segev, A. Smith Tight Bounds for Unconditional Authentication Protocols in the Manual Channel and Shared key Models. IEEE Transaction on Information Theory. Vol. 54. No 6, June 2008. pp. 2408-2425.

- V. Yakovlev, V. Korzhik, G. Morales-Luna.  Non-asymptotic Performance Evaluation of Key Distribution Protocols Based on Noisy Channels in Presence of Active Adversary. In Proc. X. Spanish Meeting on Cryptology and Information Security, Salamanca 2008, p. 63-68.

- V. Korjik, G. Morales-Luna, and V. Balakirsky, “Privacy amplification theorem for noisy main channel,” Lecture Notes in Computer Science, vol. 2200, pp. 18–26, 2001.

- D. Stinson, “Universal hashing and authentication codes,” Lecture Notes in Computer Science, vol. 576, pp. 74–85, 1992.

- V. Korjik, V. Yakovlev,  R. Chesnokov, G. Morales-Luna, Performance Evaluation of Keyless Authentication Based on Noisy Channel. International Conference of  “Mathematical Metods, Models and Architectures for Computer Network Security”, CCIS 2007. N. 1. p.

- V. Korjik and M. Bakin, “Information-theoretically secure keyless authentication,” in Proc. IEEE Symp. on IT’2000. IEEE, 2000, p. 20.

- Nisan N. and Zuckerman D. Randomness is linear in space // Journal of computer and system sciences, 1996, vol. 52, pp. 43 – 52.

- R. Raz, O. Reingold, and S. P. Vadhan, “Extracting all the randomness and reducing the error in trevisan’s extractors.” J. Comput. Syst. Sci., vol. 65, no. 1, pp. 97–128, 2002.

- Raz R., Reingold O. and Vadhan S. Error reduction for extractors // IEEE computer society press,  1999, October, pp. 191 – 201.

- Trevisan L. Construction of extractors using pseudo-random generator// Proceedings of the 31 annual ACM symposium on theory of computing, Atlanta, 1999, pp. 141 – 148.

38.	 V. I. Korzhik and G. Morales-Luna, “Hybrid authentication based on noisy channels.” // International Journal of information security, 2003, vol. 1, No. 4, pp.203 – 210.

- F. MacWilliams and N. Sloane, The Theory of Error-Correcting Codes.

North-Holland, 1977.

# Footnotes

We repeat mostly in this point the content of the same point as in [26]. It is done in order to provide an independent reading of the current paper.